## Slide 1
BAR-ILAN UNIVERSITY · FACULTY OF ENGINEERING
FinWatch
An Extensible BLE Smartwatch Platform with a Modular I²C Expansion Port
Course 83453 | Project 323 | Hardware Design Track
Omer Lazaros · Chen Leibov
Academic Supervisor: Prof. Leonid Yavitz
Project Mentor: David Freud
September 2026
Project 323
1
Github Repo: https://github.com/laserblade41/FinProj
Notes: עמר

## Slide 2
Where We're Going
FinWatch · Project 323
1
Background & Problem
Why a sealed wearable can't grow new capabilities
2
Objectives & Scope
What this project set out to build - and what it deliberately left out
3
The FinWatch Module Protocol
The core technical contribution, explained stand-alone
4
Implementation, Verification & Results
Hardware, firmware, and what has been tested so far
5
Challenges, Logistics & Conclusion
What went wrong, what we learned, and what's next
2

## Slide 3
Why Build an Extensible Wearable?
FinWatch · Project 323
The wearable engineering squeeze
Fixed board area and battery capacity - it has to fit on a wrist
Must sleep to save power, yet stay responsive to the user
Switching regulators sit centimetres from a sensitive 2.4 GHz radio
Small board area worsens both thermal behaviour and crosstalk
Every constraint pulls against each over, we need to ensure compatibility of all components
The sealed-device problem
Once assembled and sealed, the sensor set is frozen for the product's life
A new measurement idea today means designing an entirely new watch
Open wearables (PineTime, ZSWatch) open the firmware - not the hardware
Dev kits (nRF5340-DK) are fully expandable, but not wearable
Modular-phone attempts (Project Ara) failed on connector complexity at that scale
3
Notes: חן

## Slide 4
Problem Statement
FinWatch · Project 323
There is no wearable platform where a sealed, finished device can accept new I²C hardware, at runtime, from an untrusted third party - without opening the case or modifying the watch's firmware.
No case opening
No firmware update
No prior knowledge of the module
4

## Slide 5
Objectives
FinWatch · Project 323
General objective
Design, build, and verify a wearable platform that keeps real smartwatch constraints while exposing a documented, safe, self-describing expansion interface.
1
Hardware platform:
4-layer PCB: nRF5340 SoC, nPM1300 PMIC, LSM6DSOX IMU, QSPI flash, SPI touch display, pogo expansion port
2
FWMP v1:
An I²C expansion contract: electrical spec, register map, CRC-protected self-describing descriptor, host enumeration state machine
3
Zephyr firmware:
≈ 2,550 lines of C across nine subsystems implementing the watch app and the host side of FWMP
4
Fault-injection harness:
A mock transport that makes every host-side rejection path reachable without physical module hardware
5
Design-review process:
Documented hardware defects, root-cause analysis, and a pre-fabrication checklist
5

## Slide 6
Scope
FinWatch · Project 323
In Scope
One active module at a fixed I²C address (0x42)
Polled discovery since there is no dedicated interrupt line
Low-rate sensing, bounded by I²C bandwidth
Full validation of untrusted module-supplied data
Verification via mock backend + nRF5340-DK
Out of Scope (for now)
Multiple concurrent modules on the bus
An interrupt-capable expansion variant
Streaming data - audio or video
Electrical over-current / ESD protection at the port
Module authentication
6
Notes: עמר

## Slide 7
System Architecture
FinWatch · Project 323
A bidirectional level shifter connects the SoC's 1.8 V I²C bus to the 3.3 V expansion port — this is what makes the port usable by ordinary, off-the-shelf 3.3 V hardware.
7
Notes: עמר

## Slide 8
Component Selection
Every major part was chosen against explicit alternatives
FinWatch · Project 323
Function | Chosen part | Why
SoC | nRF5340 (bare IC) | Dual-core isolates BLE timing from the app; best-in-class sleep current; owns the RF design instead of hiding it in a module
PMIC | nPM1300 | One package replaces four discretes; integrated fuel gauge; native Zephyr drivers
IMU | BMI270 | Runs off the 1.8 V rail; on-sensor pedometer / ML core can keep the MCU asleep
Level shifter | PCA9306 | Purpose-built for I²C; preserves open-drain semantics in both directions
Expansion connector | 4-pin pogo | Sealed-surface contacts; no cavity through the case; cheap on the module side
8
Notes: חן

## Slide 9
The Core Contribution: FWMP
The FinWatch Module Protocol - a self-describing I²C expansion contract
FinWatch · Project 323
Electrical contract — 4 contacts, nothing more
Pin | Signal | Notes
1 | +3V3 | Watch → module; bounded module current
2 | SDA | Bidirectional, open-drain, pulled up on the watch
3 | SCL | Watch → module; watch is always bus controller
4 | GND | —
Module is an I²C target at fixed address 0x42
No dedicated interrupt line, the host discovers by polling
Watch owns the pull-ups; a module must not add its own
Logical contract — register map
Offset | Meaning
0x00–0x09 | Fixed descriptor header: magic, version, length, VID/PID, capabilities
0x0A… | TLV area, then a trailing CRC-16
0x80–0x81 | STATUS / SEQ- marks if there is any new data
0x82… | INPUT report (module → watch)
0xC0… | OUTPUT report (watch → module)
A single two-byte STATUS/SEQ read answers whether new data exists and whether it has already been seen - keeping idle polling cheap.
9
Notes: עמר

## Slide 10
Self-Description via TLV
How an unknown module tells the watch what it is
FinWatch · Project 323
Fixed Header
magic · version · length · VID/PID · CAPS
TLV Entries
NAME · INPUT_REPORT · OUTPUT_REPORT · ICON_ID
CRC-16
protects the whole descriptor
TLV catalogue (v1)
NAME: human-readable module name
INPUT_REPORT: report length + preferred poll rate
OUTPUT_REPORT: output report length
ICON_ID: index into the watch's built-in icon set
Unknown TLV types are skipped, not rejected → forward-compatible (borrowed from USB HID)
Why this beats Qwiic / STEMMA QT
Those ecosystems standardize the connector, not discovery
A Qwiic module tells the host nothing about itself; a driver must already exist
A FinWatch module's descriptor carries name, report sizes, poll rate and icon - enough to be usable the instant it's plugged in
10
Notes: חן

## Slide 11
Enumeration & the Trust Boundary
Every byte a module sends is treated as untrusted, adversarial input
FinWatch · Project 323
1
2 consecutive address ACKs → module attaches, enumeration begins
2
Descriptor validated (magic, version, length, CRC-16, TLV bounds) → ACTIVE
3
Any check fails → ERROR; not retried until the module is physically removed
4
3 consecutive NACKs, or 3 bus errors while ACTIVE ⇒ i2c_recover_bus(), back to ABSENT
11
Notes: עמר

## Slide 12
Firmware & Power Design
FinWatch · Project 323
Thread priorities (lower number = higher priority)
Thread | Prio | Responsibility
Display | 7 | Renders UI, services touch
Sensor | 8 | Blocks on IMU interrupt; samples only in an active window
Update | 9 | 1 Hz watch-face refresh; battery every 10 s
Expansion | 10 (lowest) | Presence polling, enumeration, I/O reports
Why lowest priority, deliberately
If a module holds the clock line indefinitely, it only ruins its own responsiveness , never the display, the sensor, or the watch face. BLE runs on a separate physical core, so a misbehaving module can never drop the radio link.
Adaptive polling - power vs. latency
Regime | Interval | When
Absent | 1000 ms | No module attached
Background | 250 ms | Module attached, screen not visible
Foreground | 50 ms | User looking at the module screen
Interrupt-driven motion wake
IMU's own wake-up detector asserts an interrupt on motion
Host sleeps until then - zero CPU time, zero timer wake-ups when idle
10 Hz step-detection sampling runs only inside a 3 s active window
Falls back to continuous polling if the interrupt fails to initialize
12
Notes: חן

## Slide 13
Planning vs. Execution
Original plan (five contributions) against status as of today
FinWatch · Project 323
Planned contribution | Status as of today
1. Custom hardware platform (4-layer PCB) | Revision A manufactured; power rails verified. A missing SWD header forced Revision B.
2. FWMP v1 specification | Complete: electrical spec, register map, TLV descriptor, and enumeration state machine all defined and implemented.
3. Zephyr firmware, ~2,550 LOC / 9 subsystems | Implemented and functionally verified on the nRF5340-DK, independent of the custom board.
4. Mock transport + fault-injection harness | Implemented; all six fault classes and every host-side rejection path are exercised.
5. Documented design-review process | Complete; produced directly by the Revision A SWD omission; yielded the pre-fabrication checklist.
Note: mapped from the objectives stated in the proposal / report introduction — the detailed milestone timeline follows next.
13
Notes: עמר

## Slide 14
Project Timeline
Milestones against target dates, current status as of today
FinWatch · Project 323
Jan 2025
Nordic BLE Training
Two official Nordic courses + BLE course
Done
Nov 2025
Board Schematic
Circuit design complete
Done
Nov 2025 – today
PCB Fabrication: Rev A → Rev B
Rev A manufactured; SWD fix applied; Rev B in hand, bring-up underway
Mar 2026
BLE Interface & Firmware Core
GATT services, advertising, battery notify
Done
Apr 2026
FWMP Expansion Protocol
Host-side implementation + fault injection
Done
May 2026
UI & Display
LVGL watch face, module screen, touch
Done
Jun 2026
Reference Expansion Module
Physical module build (Appendix C)
Planned
September 2026
Final Report
Write-up and documentation
In progress
● Done ● In progress ● Planned
The schedule held up well overall, the main source of delay was component/part sourcing lead times (PMIC and IMU shortages, one cancelled order), not scope or design rework. Revision B is manufactured and in hand; bring-up is in progress.
Done
14
Notes: חן

## Slide 15
Verification & Results
FinWatch · Project 323
✓
Functional verification (DK)
Full firmware- display, touch, sensor, BLE, FWMP host, run on the nRF5340-DK
Devicetree abstraction let firmware development proceed in parallel with PCB fabrication
✓
FWMP nominal path
Mock “Test Dial” module: attach → descriptor read → validated → live report exchange → detach
End-to-end proof that an unknown module becomes usable with zero host-side code
✓
Fault injection
Six injected fault classes: bad magic, bad version, bad CRC, oversize length, TLV overrun, bus error
Every host-side rejection path is reachable and exercised without physical hardware
✓
Revision A electrical bring-up
Power rails (1.8 V / 3.3 V) verified on the manufactured board
Firmware loading blocked by the missing SWD header; full functional bring-up was corrected in revision B
Physical module hardware has not yet been built — fault-injection results come from the mock transport, not real bus electrics. This is named as the top item for future work in the report.
✓
15
Notes: עמר

## Slide 16
Design Challenges: The Missing Debug Header
FinWatch · Project 323
Symptom
Revision A's power rails came up correctly, but the board could not be programmed or debugged at all.
Root cause
SWDIO and SWDCLK were simply never routed. A blank nRF5340 has no bootloader, so SWD is the only way in and an ERC only checks nets that exist, not ones that should.
Fix (Rev B)
Three signals: SWDIO, SWDCLK, and nRESET routed to 1×1 mm test pads. nRESET is included so a locked-up core can still be halted.
Component availability told the same lesson twice: a supply shortage forced a PMIC swap and a pin-compatible IMU swap. Because hardware dependencies lived in the Devicetree, the software change was confined to an overlay, not a board re-spin.
16

## Slide 17
Logistics
Improvements, challenges, budget and work plan
FinWatch · Project 323
Procurement as a design constraint
Specified PMIC and IMU were both out of stock at every distributor checked
Several suppliers would not quote single-unit student-project quantities
One order was cancelled outright, costing 14 further weeks
Availability became a primary selection criterion, not just a technical one
Pre-fabrication checklist (derived from Rev A)
SWD (SWDIO, SWDCLK, nRESET) brought out to an accessible pad set
Every rail has a test point; at least one ground clip point
Every BOM part in stock from ≥ 2 distributors, second source documented
Local decoupling within a few mm of every supply pin
Antenna keepout clear on all layers; RF match is controlled-impedance
17

## Slide 18
How FinWatch Compares
Honest about where it's behind and precise about where it's new
FinWatch · Project 323
Property | PineTime | ZSWatch | Dev Kits | FinWatch
Wearable form factor | Yes | Yes | No | Yes
Sensor richness / maturity | Basic | Rich, mature | Rich | Basic, prototype
Expansion without opening the case | No | No | n/a | Yes
Third-party modules, no first-party driver | No | No | No | Yes
Runtime device discovery | No | No | No | Yes
Self-describing descriptor | No | No | No | Yes
ZSWatch shares the same SoC, RTOS, PMIC and flash part, is more mature. The claim here is narrow and specific: not a better watch, but a sealed device that can use hardware its firmware has never seen.
18
Notes: חן

## Slide 19
Conclusion
FinWatch · Project 323
A sealed watch can use hardware its firmware has never seen, discovered, validated, and made usable at runtime through four contacts and a self-describing descriptor.
Recommendations, aligned to each objective
Hardware platform:
Complete Revision B bring-up and validate the RF match against the on-board antenna
FWMP protocol:
Build a physical reference module (Appendix C) to expose real electrical hot-plug behaviour
Firmware:
Move step counting fully into the IMU's embedded pedometer to cut active-window CPU time
Safety / robustness:
Add current limiting and ESD protection at the port; the trust boundary is still only logical
Scale:
Explore multi-module addressing and an interrupt-capable variant to remove idle polling cost
19

## Slide 20
Thank You
Questions?
Omer Lazaros · Chen Leibov
Academic Supervisor: Prof. Leonid Yavitz email: leonid.yavitz@biu.ac.il
Project Mentor: David Freud email: david.freud@mail.huj.ac.il
Course 83453 · Project 323 · Faculty of Engineering, Bar-Ilan University
20